LIGHT STUDIO L010

LED PAR 54*3W (R G B W)

User Manual

SPECIFICATIONS Voltage: AC-220V/240V 50-60Hz Rated power: 180W Light source: LED-RGBW 54*3W Beam angle: 15\45 Brightness adjustment : 0-100 % Strobe speed: 0-20HZ Channel mode: 8 channel mode Control mode standard DMX512 signal, master and slave, voice control . Thermostatic protection: cooling at 70 C Improve lamp life Protection class: IP54 Size: 24CM 24CM Weight: 1.25KG

DMX Values and Function 8 CHANNELS

| Channel | Channel Value | Function |
| --- | --- | --- |
| 1channel | 0--255 | R G BW Tune ON/OFF |
| 2channel | 0--255 | Red (0%--100%) Green lasting lighted，From dark to bright |
| 3channel | 0--255 | Green (0%--100%) Green lasting lighted，From dark to bright |
| 4channel | 0--255 | Blue (0%--100%) Green lasting lighted，From dark to bright |
| 5channel | 0--255 | White (0%--100%) Green lasting lighted，From dark to bright |
| 6channel | 0--255 | slow to fast |
| 7channel | 0--255 | Speed(slow to fast ) |
| 8channel | 0--5 | nop |
|  | 6--69 | Three color pulse change |
|  | 70--129 | Seven color jumped change |
|  | 130--189 | Seven color gradient |
|  | 190--249 | RGB Chase |
|  | 250--255 | Sound ON |

Adde-DMX address setting menu

# Text boxes

A001

A512

Address

de01

Run Color

de99

SoU01

SoU09

Sound

Strobe

Fh99

Fh01

Red

r255

Green

G255

b255

Blue

r001

G001

b001

U001

U255

White